## Slide 1
1. Prepare 3 USBs for update.
2. Copy files from PC to USB.
- 1st : LG_PMS_DEU15_10.05.6501.R1367_R1754_1919_191A
- 2nd : LG_PMS_DEU15_10.05.6501.R1367_R3XXX_191A_1920
- 3rd : LG_PMS_DEU15_10.05.6501.R1367_R3755_1920_1920
3. Inserted order is very important to update.
4. Refer to next page for update process.
5. Repeat 3 times using 3 different files.
6. Check the SW version.
Last page shows SW information for each case.
Update Guide

## Slide 2
2. Remove the inserted WLAN dongle and then insert the included USB memory.
1. After connecting all the wires (PV, Grid, Battery, BMS, Meter), Turn on the Product
3. If the update is in progress, LED lite one by one.
The update takes time about 4 to 5 minutes.
4. If the update is done, LED of "Solar" lite on and LED of "Power, WLAN" is blinking
5. Now, Update is done. Remove the inserted USB memory and then insert the WLAN dongle.
Update Guide

## Slide 3
SW information
< Final Image >